ANNEX 3

| Table 1 - A420 Headington Road/London Road - NORTH SIDE |
| --- |
| From | To | Proposed Changes |
| Headley Way junction | Sandfield Road junction | Remove the existing off-carriageway segregated cycle track and create as footway |
| Sandfield Road junction | Latimer Road Toucan crossing | Remove the existing off-carriageway segregated cycle track and create an un-segregated cycle/footway facility between these two points. |
| A point 35 metres east of the Latimer Road junction | A point 31 metres west of the Osler Road junction | Reduce the width of the existing off-carriageway segregated cycle track from 1.60 metres to 1.20 metres. Remaining area to be designated footway (width varies from 1.90 metres to 2.30 metres). |
| A point 31 metres west of the Osler Road junction | Osler Road junction | Create an off-carriageway segregated cycle track 1.20 metres wide. |

| Table 2 - A420 Headington Road / London Road - SOUTH SIDE |
| --- |
| From | To | Proposed Changes |
| Westbound approach to the Latimer Road Toucan crossing | Latimer Road Toucan Crossings | Create a 15 metre length of segregated off-carriageway cycle track, 1.20 metres wide, 2.70 metres long accessed by a section of dropped kerb. |
| Latimer Road Toucan crossing | Headley Way junction | Reduce the width of the existing segregated off-carriageway cycle track from 2.50 metres to 1.20 metres. Remaining verge area to be designated as footway (width varies from 2.40 metres to 3.60 metres) |
| Headington Road Service Road/Valentia Road | Gipsy Lane junction | Create a 2.00 metre wide cycle track to link Headington Road with the Service Road just west of the junction with Brookside. At the west end of the Service Road create a new section of 2.00 metre wide cycle track to allow cyclists to access the advanced stop line on the westbound approach to the Gipsy Lane junction on Headington Road. |

ANNEX 3

THAMES VALLEY POLICE

Division/Station :	 Traffic Management, Witney

From :	 T.N. Currell	To :	Superintendent Roads Policing

Bicester

Ref :	TM 1064/2007 	  HQ178/1/35                             Date : 28th November 2007	     Tel.No.	07970 145775

Subject  :

Proposed changes to Headington and London Road – Bus Lane & new 20mph Speed Limit

This report is in response to a letter of consultation and drawing nos. B0210200/S2/CON/TRO/005 & 006 received from Jacobs.

# History

There are no previous papers on file in relation to this particular subject.

Investigation

Oxfordshire County Council plan to improve Headington Road and London Road between Pullens Lane and Osler Road. The proposals cover the provision of a bus lane, 20mph speed limit and some changes in cycling facilities.

The proposed bus lane will run between Gypsy Lane and Osler Road. It will vary in width from 3m. to 3.5m. In places the advisory cycle lanes, off carriageway segregated cycle lanes will be incorporated into the bus lane. At the Headley Way junction there will be an advanced stop area for cyclists with an advisory cycle lane through the junction (north and south side). There will be new unsegregated cycle/footway facilities near to the Latimer Road Toucan crossing (north side), segregated ( south side) and an extension of the off carriageway segregated cycle lane to the junction of Osler Road. Some of the existing off carriageway segregated cycle lane is to be reduced in width to 1.2m. Removal of the on carriageway advisory cycle lane from Headley Way junction to Gipsy Lane and replacement with alternative route along the service road.

The 20mph speed Limit will be from Pullens Lane to Headley Way junction.

Consultation

I have spoken to Elio Astone with regard to the proposals.

Conclusion

Speed data has been received from O.C.C. with reference to the speed of traffic using Headington Road and London Road. However this data is from 2000. The 85th percentile speed and average speed indicate that a 20mph speed limit is unlikely to be effective without engineering measures or constant

enforcement. The current speed of traffic is a reliable indicator of how acceptable a new speed limit would be. It is therefore very important that the existing speed of traffic is within the guidelines for the introduction of such a speed limit (DfT Circular 1/2006 sec.5.1 72 -75).

Thames Valley Police have no structured enforcement regime for 20mph speed limits.

Cycle lanes less than 1.5m. wide cannot easily accommodate tricycles or child carrying cycle trailers.

Bus lanes below 4m. in width generally cause buses to leave the bus lane in order to overtake cyclists. This may be difficult if the adjacent lane is congested and could cause delay for the buses etc.

There is considerable potential for conflict between pedestrians and cyclists near to the Latimer Road Toucan crossing and Osler Road.

Recommendations

That a letter and a copy of this report be sent to Elio Astone, Jacobs for his attention.

T.N.Currell

Traffic Management