| Respondent | Support Proposal | Comments | Officer comments |
| --- | --- | --- | --- |
| Resident, Burcot Lane | YES | Requested further restrictions to HGV traffic along Burcot Lane in both directions. | If the proposed scheme is adopted HGV traffic can be monitored after the prohibition of right turns on the A4074 has been introduced. |
| Resident, Burcot Lane | YES | Requested further restrictions to HGV traffic along Burcot Lane in both directions. Also requested a bus stop on the A4074 and a cycle rack facility on the proposed self enforcement island. | Monitoring as above. Discussions have been held with the Public Transport team and there are no current proposals to provide a bus stop at the junction. A cycle rack is considered to be a hazard to pedestrians and cyclists in dark conditions as the locality is unlit. |
| Thames Valley Police | YES | Requested physical measures be included to ensure that the Order is as self enforcing as possible, i.e. traffic island. | The design was modified by extending the A4074 face of the island to discourage unlawful right turning. |
| Burcot Farm | YES | Need to ensure access arrangements to farm properties and fields are maintained. | Agreed. Access arrangements will be considered and catered for with final design considerations. |
| Clifton Hampden Parish Council | YES | Support the proposal. Also requested a bus stop on the A4074 and a cycle rack facility on the proposed self enforcement island | Discussions have been held with the Public Transport team and there are no current proposals to provide a bus stop at the junction. |
| Member of Oxonian Cycle Club | NO | Traffic speed on the A4074 is too fast which deters walking and cycling. A cheaper solution is to lower the traffic speed by narrowing the carriageway, removing the centre line roadmarking, use cycle lanes and removing priority. A right turn restriction will inconvenience users of the turn, increase their journey distance, promote car users and make the A4074 traffic speed faster, increasing the risk of fatal accidents. Excessive increase of highway surface, widening and proliferation of intrusive engineering clutter. Prevention of journey directions for all. No provision for cyclists. Cyclists who choose to perform a right turn will be made ‘outlaws’. Excessive use of marker posts is visually intrusive, aggressive and objectionable. Use of thermoplastic screed is unnecessary and objectionable. No attempt to be sympathetic to local situation by utilising shrubs and trees. To allow grass not to be mowed. This is an unusual way to restrict the junction and to make it visible indicates that the solution is inappropriate. | Recent surveys carried out on the A4074 show the traffic is generally within the speed limit. The purpose of the scheme is to eliminate accidents involving vehicles turning right from A4074 into Burcot Lane and to prevent a fatal accident. Reducing traffic speed on the A4074 will require police enforcement. Thames Valley Police (TVP) has requested that any new measures should be self enforcing. The island in the junction is a self enforcement feature which is encouraged by TVP to minimise the impact on their resources. Agreed to minimise clutter and the number of road markers will be reviewed. A4074 southbound traffic only will be affected. There will be an additional journey length of 1.4 miles via Berinsfield Roundabout. This is a 60 mph limit location. Any formal provisions could be difficult to justify, however it can be looked at during the detail design stage. Noted. The number of road markers will be reviewed. To be reviewed subject to Safety and Vulnerable Road Users Audits. Agreed to soften the enforcement island but a balance has to be reached to ensure it is conspicuous under all lighting conditions especially in an unlit rural setting and to ensure there is sufficient visibility for all road users using the junction. |