#### ANNEX 1

##### PROJECT APPRAISAL 	APPRAISAL NO: H188

## Name of the Scheme:	London Road Corridor (Pullens Lane – Osler Road)

Basis of Estimate: 	Similar scheme in Aylesbury

Start Year: 	2007/08.

DESCRIPTION OF PROJECT

- This scheme is to develop the Headington Road / London Road corridor between Pullens Lane and Osler Road to make bus journeys quicker and more reliable and improve road safety for all road users.  This will be achieved by the following:

  - Outbound bus lane from Gipsy Lane to Osler Road

  - Bus Gate arrangements to re-introduce buses in to the general traffic flow

  - Enhancements to the street environment in the area close to Oxford Brookes University (to be paid for by the university)

  - New and improved pedestrian crossings

  - Improving the working of the road’s traffic lights to give buses greater priority

  - On and off-carriageway cycle routes

  - New 20mph speed limits

NEED FOR PROJECT

- A scheme for improvements to the London Road corridor is a key part of the County Council’s second Local Transport Plan and its Capital Programme.  The delays experienced by the large numbers of people travelling along the route by bus are very significant and, as a result, there is a continuing major impact on the reliability and attractiveness of buses as an alternative to the car for journeys in this area.  The accident rate on the London Road is around twice the national average for a major route such as this.

CONSISTENCY WITH SERVICE STRATEGY

- The scheme is included in the County Council’s transport programme for 2006-2011 that supports the delivery of the aims and objectives of the Local Transport Plan for the same period.  These are:

- Tackling congestion;

- Reducing road casualties;

- Improving accessibility;

- Improving air quality; and

- Improving the street environment

The scheme is expected to:

- Reduce the congestion experienced by users of the London Road (particularly bus users) and in so doing improve access to the services along or close to the corridor (shops, colleges, hospitals);

- Improve the road safety accident record along the corridor;

- Improve the street environment along the corridor.

ENVIRONMENTAL AND OPERATIONAL FACTORS

- The proposals lie within the existing road corridor so minimising any further impact on the area. Two trees will be lost due to the works but efforts will be made to identify replacements in the same or other areas if possible. Improvement of the bus services will offer an attractive alternative mode of transport to the car for those travelling to destinations along the corridor.

- It is anticipated that most of the construction works can be undertaken whilst maintaining a 2-way flow of traffic. Traffic delays will therefore be kept to a minimum.

OTHER REASONABLE OPTIONS

- In 2005 a study was undertaken to develop measures for London Road that would:

  - Improve public transport journey time, reliability and operation, thus improving the desirability and attractiveness of bus services resulting in the potential increase in bus patronage;

  - Address road safety considerations, specifically at locations where particular issues have been identified; and

  - In appraising the options, ensure that the impact on other road users (including pedestrians) is identified and considered appropriately.

- Two different design approaches were developed for the corridor. These were:

Approach 1: This was an engineering-based approach, which reviewed what could be achieved to meet the study objectives, assuming the same level of traffic was maintained on the corridor as at present. Measures proposed for the corridor included bus lanes and lay-bys, pedestrian crossings, and lowering the speed limits in certain sections.

Approach 2: This was a traffic management based approach, which reviewed what could be achieved on the corridor, should the level of traffic be reduced. It proposed restricting access to through traffic in the Headington central area, and permitting access to buses, taxis and emergency vehicles only on a similar principle to Oxford High Street. This would facilitate priority for these vehicles without needing such heavy engineering measures, as required in Approach 1.

- Consultation on the study was carried out in June and July 2005 and comprised of stakeholder meetings, public exhibitions and an internet web site.

The results from the consultation indicated general overall support for the measures outlined in Approach 1. Approval to proceed with Approach 1 was granted by Cabinet in November 2005. A do-nothing option would only result in further congestion on the corridor adding additional delay to bus services. This decrease in service would lead to more use of private vehicles on the route and the potential of more accidents.

LAND

- No land outside the existing Highway is required to implement the scheme.

FINANCIAL AND STAFF IMPLICATIONS

- Finance for the scheme has been identified in the Local Transport Programme from 2006/07 through to 2009/10. This is made up from SCE and developer contributions. A full financial appraisal is shown below.

- Enhancement of the area outside Brookes University will be financed through a Section 278 Agreement to cover design, construction and future maintenance costs. The scheme will be the subject of a competitive tendering process under the NEC 3 form of Contract. Design, tender procedures and site and contract supervision will be undertaken by resources from Oxfordshire Highways.

TIMING/PHASING

- The scheme is programmed to go out to competitive tender in February 2008, with a view to starting construction in June 2008. The construction period is estimated to be approximately 6 months.

STEVE HOWELL

Head of Transport

Environment & Economy

Contact Officer: 	Mike Collins, Principal Engineer, Tel: 01865 815877

November 2007

Financial Project Appraisal

| Name of the Project: London Road Corridor (Pullens Lane to Osler Road) |
| --- |
| Appraisal No: H188……………………………………………………………………. |
| Status: Detailed | Date: September 2007 |
| Capital Expenditure and Financing |  |  |  |  |  |  |  |
| Project Expenditure | 2006/ 07 | 2007/ 08 | 2008/ 09 | 2009/ 10 | 2010/ 11 | 2011/ 12 | Total |
|  | £'000 | £'000 | £'000 | £'000 | £'000 | £'000 | £'000 |
| Construction |  |  | 2701 | 69 |  |  | 2770 |
| Fees | 45 | 292 | 100 | 12 |  |  | 449 |
| Total Estimated Payments | 45 | 292 | 2801 | 81 |  |  | 3219 |
| The Construction Costs per square metre is …………… gross/net. |  |  |  |
| Project Funding | 2006/ 07 | 2007/ 08 | 2008/ 09 | 2009/ 10 | 2010/ 11 | 2011/ 12 | Total |
|  | £'000 | £'000 | £'000 | £'000 | £'000 | £'000 | £'000 |
| Borrowing Approval | 45 | 292 | 2351 | 81 |  |  | 2769 |
| Capital Receipt(s) |  |  |  |  |  |  |  |
| Contributions from Developers |  |  | 450 |  |  |  | 450 |
| Grant(s) |  |  |  |  |  |  |  |
| Revenue Contributions |  |  |  |  |  |  |  |
| Other |  |  |  |  |  |  |  |
| Total Financing | 45 | 292 | 2801 | 81 |  |  | 3219 |
| Revenue Implications |  |  |  |  |  |  |  |
| Corporate Costs | 2006/ 07 | 2007/ 08 | 2008 09 | 2009/ 10 | 2010/ 11 | 2011/ 12 | Total |
|  | £'000 | £'000 | £'000 | £'000 | £'000 | £'000 | £'000 |
| Capital Financing (Cost of Borrowing) | 1 | 11 | 89 | 243 |  |  | 243 |
| Service Implications | 2006/ 07 | 2007/ 08 | 200 09 | 2009/ 10 | 2010/ 11 | 2011/ 12 | Full Yr Effect |
|  | £'000 | £'000 | £'000 | £'000 | £'000 | £'000 | £'000 |
| Employees |  |  |  |  |  |  |  |
| Running Costs |  |  | 14 | 14 | 14 | 14 | 14 |
| Income |  |  |  |  |  |  |  |
| Net Cost/(Savings) to Service |  |  | 14 | 14 | 14 | 14 | 14 |
| Staffing | 2006/ 07 | 2007/ 08 | 2008/ 09 | 2009/ 10 | 2010/ 11 | 2011/ 12 | Full Yr Effect |
|  | F.T.E. | F.T.E. | F.T.E. | F.T.E. | F.T.E. | F.T.E. | F.T.E. |
| Additions/(Savings) resulting from the project | 0 | 0 | 0 | 0 | 0 | 0 | 0 |